## Slide 1: Cloud Router
Cloud Router is a distributed and fully managed offering that provides Border Gateway Protocol (BGP) speaker and responder capabilities.
It works with Cloud Interconnect, Cloud VPN, and Router appliances to create dynamic routes in VPC networks based on BGP-received and custom learned routes.
Cloud Router and the Andromeda network virtualization stack work together.
Cloud Router (The Control Plane): It runs the BGP sessions, learns routes from your network, and decides on the best paths.
Andromeda (The Data Plane): It takes the routing decisions from Cloud Router and executes them at lightning speed, forwarding the actual data packets.

## Slide 2: Cloud Router (Cont.)
Dynamic Routing Options
  Regional: Shares routes only for subnets in the region where Cloud Router is provisioned
  Global: Shares routes for all subnets in the VPC
Route advertisement (on BGP session or Cloud Router level)
  Default: Advertises subnets according to the selected routing option
  Custom: Customize which subnets and IP ranges to advertise, for example, when you want to skip advertising specific subnets or when you want to advertise subnets in different BGP sessions for separation purposes

## Slide 4: What is BGP
BGP is the official routing protocol of the internet. It's how different networks (called Autonomous Systems) share information about which IP addresses they can reach.
Instead of manually setting up static routes (which is tedious and error-prone), BGP allows your network and Google's network to dynamically learn from each other. New routes are discovered and shared automatically.
If you add a new subnet in your VPC, Cloud Router sends a BGP UPDATE message to your on-prem router so it knows about the new network.
If a VPN tunnel or Interconnect connection fails, the BGP session on that link goes down, and the routes are automatically withdrawn. Traffic then fails over to a redundant path if one exists.

## Slide 5: Autonomous System
An Autonomous System (AS) is a large, independent network with a single, clear administrative authority.
A major Internet Service Provider (ISP) like Airtel or Jio.
A huge tech company like Google, Microsoft, or Amazon.
A large university or government institution.
Autonomous System Number
An ASN is simply the unique number assigned to an Autonomous System. When two systems establish a BGP session to talk to each other, the first thing they do is announce their identities using their ASNs.
Public ASNs: These are globally unique numbers assigned by internet authorities (like IANA). They range from 1 to 64511.
Private ASNs: Just like private IP addresses (192.168.x.x), these are reserved for internal use.
The private range is 64512 to 65534

## Slide 6: BGP Identifier Range
Each Cloud Router has a BGP identifier, also known as a router ID.
The BGP identifier is unique to each Cloud Router in your Virtual Private Cloud (VPC) network
You can assign an explicit BGP identifier range to your Cloud Router. If you do, your Cloud Router is assigned a stable BGP identifier from the assigned range.
Unless you've configured an explicit BGP identifier range, Cloud Router might change the automatically generated router ID in the following circumstances:
  You add a BGP session
  You remove a BGP session
  During periodic maintenance

## Slide 7: BGP Timers
Keepalive timer
BGP systems exchange keepalive messages to determine whether a link or host has failed or is no longer available. In conjunction with the hold timer, the keepalive timer indicates whether a router is reachable to its BGP peer.
The default value is 20 seconds. Google recommends setting the keepalive timers to the same value on your on-premises router and the Cloud Router.
Hold timer
This timer tracks the minimum amount of time since the last successful keepalive message was detected. It indicates the length of time that a Cloud Router or your on-premises router should wait, absent a graceful restart notification, before removing the routes that it learned from the other router.
Cloud Router sets this value to the value of its configured keepalive timer multiplied by three.

## Slide 8: BGP Timers (Cont)
Graceful restart timer
This timer tracks the amount of time that a router waits after it receives a graceful restart notification (TCP FIN or RST packet) from another router.
When establishing a new BGP session, each router communicates its own graceful restart timer value to the peer router through the BGP OPEN message.
Cloud Router supports graceful restart, and the Cloud Router graceful restart timer is set to 120 seconds. Every Cloud Router sends a graceful restart notification before each software maintenance event.
Stalepath Timer
This setting determines how long a router waits before deleting learned routes after it receives an end-of-record (EOR) message from the other router.
Google recommend setting the stalepath timer to 300 seconds on your on-premises router to match the setting for the Cloud Router.