## Slide 1: MultiProtocol BGP (MP-BGP)
By default, when you create a BGP session in Cloud Router, you create an IPv4 BGP session. The IPv4 BGP session, by default, exchanges only IPv4 routes.
However, you can configure the IPv4 BGP session to exchange IPv6 routes by using multiprotocol BGP (MP-BGP).
To enable IPv6 route exchange on your IPv4 BGP session, you need to configure a IPv4 and IPv6 (dual stack) HA VPN tunnel or Dedicated Interconnect VLAN attachment.
Similar to IPv4 BGP sessions, you can also configure an IPv6 BGP session with multiprotocol BGP (MP-BGP). However, with MP-BGP over IPv6 BGP sessions, you exchange IPv4 routes over an IPv6 BGP session.

## Slide 2: MultiProtocol BGP (MP-BGP) Cont.
You can also establish both an IPv4 BGP session and an IPv6 BGP session in parallel.
Each session exchanges only routes for its own address family. IPv4 BGP sessions only exchange IPv4 routes, and IPv6 BGP sessions only exchange IPv6 routes. You can't use MP-BGP in individual BGP sessions.
Suppose the dataplane experiences an IPv4-only traffic outage.
  An IPv4 BGP session with MP-BGP withdraws the IPv4 routes, but also withdraws the IPv6 routes.
  An IPv6 BGP session with MP-BGP does not go down and does not withdraw any routes, either IPv4 or IPv6. Subsequently, only IPv4 traffic drops.

## Slide 3: MD5 Authentication
By default, Cloud Router BGP sessions are unauthenticated.
However, when you use Cloud Router with certain products, you can optionally configure your BGP sessions to use MD5 authentication.
When you configure a session to use MD5 authentication, you provide a secret shared key—a key that you use when configuring Cloud Router and again when you configure your peer router.
After you complete the required setup steps, Cloud Router uses that key to authenticate the BGP peer.
You can add MD5 authentication when you create a peer. You can also add authentication to an existing session, change the key that a session uses, or remove authentication.